## Slide 1
Section 4
Delineation and Selection of Equipment for Damp Situations

## Slide 2
Section 6 of the Wiring Rules contains the requirements for installations in damp situations and other areas where special installation requirements must be met. The defined special situations include situations where moisture is either permanently present or intermittently present, i.e:
Swimming pools.
Spa pools.
Baths, showers and other fixed water containers.
Fountains and water features.
Refrigerated rooms.
Sauna baths.
General hosing areas

## Slide 3
International Protection Ratings
Electrical accessories installed in damp situations are required to conform to an International Protection Rating (IP Rating) as provided for in AS/NZS 3000 (see appendix G – Degrees of protection of enclosed equipment).
An International Protection (IP) rating is assigned to a particular zone. The degrees of protection provided under IP classifications uses the letters IP followed by two numbers. The first number indicates the degree of protection from contact and the second indicates the degree of protection from the ingress of liquids.
For example, the classification IP56 would indicate complete protection against contact with live parts (5) and protection from water from high pressure water jets (6).

## Slide 4
Classification of Zones for Damp Situations
The delineation damp situations is based on the AS/NZS 3000 classifications of zones. The zones determine the degree of increased risk of electric shock and provide guidance for the selection and installation of electrical equipment within the specified locations.
In general, Zone 0 is the area of the interior of the water container while Zone 1, Zone 2 and Zone 3 extend both horizontally and vertically from Zone 0

## Slide 5
Now answer the questions on page 57.

## Slide 6
THE END